SeaSlug Manual
March 15, 2015

# Launch Supplies Checklist
## Large black tub
(2x) 50ft of black rope / Foot inflator, hose, and connector for the fender / WD40 / Wire brush	Shore power adapter / Lifejacket / Pillow / 2 towels / Extension cord (>50ft) / Rubber & metal mallet

## Large red Stanford toolbox (electronics & tools)
Extra 8x AA batteries in their own sealed baggie / DX5 RC Transmitter / CANmodul USB<->CAN adapter & CANaconda / USB/RS232 adapter / Main & backup USB wireless controller / Main & backup PICkit3 w/ USB & extension cable / 2x walkie-talkies / Multimeter / Saleae logic analyzer / 5/16” nutdriver	Small red flathead screwdriver (for the ACS300 & IMU) / Small Philips screwdriver (for the 2035) / Big Philips (for the hatch screws/electrical terminals) / Two small adjustable wrenches (for various nuts) / Yellow wire strippers / Small red pliers and big black pliers / Headlamp

## Small red toolbox (cables/spare parts)
Female DB9<->3-pin CAN adapter / RS232 adapter for the ACS300 board / E-stop button / Bag of screws (for the main hatch) / Spare 0.1” signal connectors/jumpers (2-pin jumper, male-male, female-male)	Spare CANodes, 5V regular, and shields (duplicate of everything onboard) in an anti-static bag / Spare CAN parts/cables/connectors in a baggie / Spare power parts/cables/connectors in a baggie

## Red backpack
My work laptop & power adapter / Notebook & pen / Food & water / Cellphone & wallet / Sunscreen	USB thumbdrive / Extra pair of pants, warm sweatshirt/jacket / This launch manual (printed in a 3-ring binder) / Binoculars / Hat and sunglasses

## Loose
- GPS/WSO100 stub mast
- Groundstation computer, all sealed up
- The mast (keep its 3 pipe clamps in the top of the large red toolbox)
- Black 10' fender

# Launching the boat (2 people)
## Part 1 - Prelaunch
1. Park the vehicle with trailer somewhere out of the way.
2. Remove the top hatch and store in the vehicle.
3. Secure and connect both the stub mast and the true mast.
4. Remove the black straps securing the SeaSlug to the trailer.
5. Secure the ropes, one to the front u-ring and one to the rear, using the two-half-hitches knot. Coil the remainder and leave readable from the very front of the bow.
6. The launcher driving the boat needs to change into shorts and shoes that can get wet.
## Part 2 – Launch
1. Partially (1/3) inflate the 3m black bumper and bring out to the dock and secure it in between two cleats using the black loop on one end and the green string on the other. Be sure to place it far enough from the ramp to fit a couple of boats. Also staying in the shade is nice.
2. Drive the vehicle up to the boat ramp and back it up.
3. Chock the trailer tires.
4. Disconnect the trailer hitch and pull forward >= 3m.
5. Remove the trailer hitch extension and secure it to the trailer.
6. Back the vehicle up and resecure the hitch.
7. Leave the 3rd wheel of the trailer down, but cranked all the way up.
8. Remove the trailer's wheel chocks.
9. Backup until the water reaches a few centimeters above the bottom of the U-bracket on the trailer.
10. Park the van and chock the front wheels.
11. The van driver gets out and disengages the front hook of the SeaSlug and throws both lines of rope to another person waiting on the dock.
12. The docker tows the SeaSlug over to where the bumper is and docks it snug against the dock (the boat will list slightly, but that is fine). Use a cleat-hitch to secure the fore and aft ropes snug, < 45o angle. Stow the ropes in nice coils near the cleats.
13. Get back in the vehicle, unchock the wheels, and reverse the trailer hitch process.
# Recovering the boat (2 people)
## Part 1 - Recovering
1. Leave the boat secured tight against the dock and turned off.
2. Using both people get the extended trailer onto the vehicle. Make sure the 3rd wheel is down but cranked all the way up.
3. Back the trailer into the water until the water covers the bottom of the u-bracket a few centimeters. This is fine if it's only during a tidal surge.
4. Have the docker undock the boat and move the boat forward until it sits a few meters behind the end of the trailer.
5. The docker should throw the forward rope to the launcher, who is waiting in the water on the front of the trailer. Once they have the rope, they should throw their aft rope onto the boat.
6. They guide the boat in straight to make sure the prop doesn't get damaged and untie the front line.
7. Then the front crank hook is attached and the boat is ranked up and the forward eyemount is seated up above the pulley for the crank hook ribbon.
8. Now the launcher can tow the boat out of the water. The hitch must be switched back to the main trailer hitch before pulling all the way out of the launch ramp.
## Part 2 – Securing
1. Retrieve all supplies from the boat and the dock and secure them in their containers in the vehicle.
2. Strap down the sides of the SeaSlug to the trailer with the black cinch ropes.
3. Secure the internal electronics compartment.
4. Secure all hatches (main hatch with at least 3 screws).
5. Disconnect the stubmast and rear rope.
# Final Testing Checklist
This should be done a day or two before the launch and then the SeaSlug should remain undisturbed until launch day.
Groundstation	In sealed enclosure w/ radio connection / Receives telemetry from all systems (test w/ all real sensors and in HIL) / Retrieves/modifies waypoints / Retrieves/modifies parameters (esp. disabling autonomous mode)
Primary controller	Rudder calibration / Rudder control / Switching modes / Throttle
Secondary controller	Transmitter calibration / Rudder calibration / Rudder control / Throttle control / Overrides primary controller when on / Can be on but disabled without controlling anything
Autonomous control	Runs a complete waypoint set in HIL when connected to the actuators
Datalogger	Receiving telemetry. Test with a groundstation connection to the output port as well as a watching the LED indicators on it.
Return-to-base functionality	Triggered when pulling the e-stop / Triggered when communications are lost to the rudder node for > 1s / Triggered when the groundstation disconnects for >= 30s / Triggered when the GPS cuts out for >= 10s

# Preflight checklist
- Stub mast secured with sensors connected
- Rudder hatch secured
- Main mast secured
- Front IMU hatch secured
- Electronics hatch secured
- Battery ballast tray secured
- Rudder calibrated
- Primary controller check (full rudder/throttle range, autonomous mode switching, can calibrate)
- Emergency controller check (full rudder/throttle range, autonomous mode switching, can calibrate)
- GPS status check (see in groundstation)
- Supplies onboard: RC transmitter (waterproof), primary controller (waterproof), groundstation (waterproof), space batteries (waterproof), cellphone (waterproof), radio (waterproof)
- Lifejacket on
- Actuator and electronics batteries on
- Groundstation operational and receiving telemetry at correct rates
- Electronics are all secured inside the SeaSlug
- Fore and after ropes coiled and within reach
- E-stop disengaged
- The IMU readings in QGC look stable and correct

# Operating Guide
Operating the vessel can be broken down into three main modes of operation: manual control, autonomous control, and emergency manual control. Further details on each mode is given below.
## Manual Control
Manual control is done through the QGroundControl program. It can communicate with joysticks, gamepads, and other controllers to control any vehicle it connects to. While the SeaSlug uses some custom messages to output telemetry, the bulk of the interaction with the vehicle uses the common messageset which is always available in QGC.
To enable manual control, simply connect a suitable PC controller over USB, open Settings and map the throttle and yaw values to the desired axes. Note that L1 on the Logitech F710 controller is used to enable setting the throttle value, so if that's not held down when moving the throttle axis, nothing will happen. Additionally, button 8 is hard-coded to activate the rudder calibration regardless of controller. Both of these were done so as to support QGC out-of-the-box.
## Autonomous Control
Autonomous control can be enabled through the QGroundControl groundstation computer. It can either be enabled by setting the AutoMode parameter. The controller can also be used to toggle the state of the vehicle by mapping the Toggle Autonomy action to a button on it. This is the preferred method and it guarantees that manual control can be switched to in case of problems with the autonomous controller.
QGroundControl provides methods for changing onboard parameters, managing waypoints, and visualizing data. Most of the built-in features are supported with the SeaSlug, and the user should be referred to the QGC documentation.
## Emergency Control
In an emergency, where the vessel is out of control or needs to be restrained for some other reason, the simplest thing to do is hit the e-stop button located to the rear of the vessel. This will disable the propeller motor controller and all systems will be held in reset. This should also center the rudder, making towing the vessel easy if it's required.
In a non-emergency situation or one in which direct control of the vehicle is desired, the backup/secondary/emergency controller can be used. It has its own CANode so that it can talk directly to the rudder and propeller controllers and bypass the primary controller completely. When this happens, the PrimaryNode goes into reset. This allows the boat to also be controlled in situations where the PrimaryNode is not responding, which is very useful for testing purposes.
The emergency controller is a Spektrum Dx5 RC transmitter with a receiver mounted inside the vessel. The range should be good out to at least 50m. It should be labeled, but the main controls are:
- Left-stick, up/down controls the throttle
- Left-stick, left/right controls the rudder angle
- Switch 1 is an enable, when this is active this controller has control of the vessel. If you are concerned about a situation it is advised to keep this controller on and disabled. Flicking this switch can provided faster vehicle response than going through the primary controller.
- The right-analog stick can be used to toggle the rudder calibration. A left-right-left motion will toggle calibration.
# Simulation
Simulation is split up into three sections: full software simulation, half hardware-in-the-loop, full hardware-in-the-loop. These simulators are all contained within the basic_model folder. The simulation_constants.m file is also here, which sets some basic state data for the vehicle at the start of simulation. And the controller itself is located in the primary_node folder.
## Full Software Simulation
The full simulation environment is contained within the Full_sim.mdl file. It is merely scaffolding supporting the connection of the Plant.mdl implementing the environment & vessel simulation with the controller.mdl. Running this model will generate output data similar to what's recorded during an actual boat launch. The Full_sim*.m files are visualization aids for viewing the results of the simulation. Further investigation can be done manually.
## Half HIL
Hardware in the loop simulation is first done with just the controller moved onto the real hardware. There are no connections from the controller to real actuators or sensors at this point. Testing this is done by using the HILNode to translate the UDP connection from Simulink to the CAN bus messages that the PrimaryNode works on. Note that in this mode the controller has no idea that it is running in simulation. This means that the exact same procedure to run & operate the SeaSlug applies here!
The HILNode needs to be programmed, powered on, and connected over Ethernet to the simulation computer. It also needs a CAN connection to the PrimaryNode, which is also powered on. The groundstation, along with the primary controller, is also required at this stage and should be connected over serial or radio. Note that this CAN connection needs to be a proper bus with the two 120Ω resistors for this connection to work. With the system connected as so, running the HIL_sim.mdl file will run the Plant onboard the simulator computer and leave the controller to process the data offboard. The HILNode has been programmed to use the same transmission rates as used by the actual hardware sensors.
Note that for HIL to work properly, the GPS, IMU, and DST800 cannot also be transmitting on the bus. There are reset flags for each of those peripherals, so check the NODE_STATUS message in QGroundControl. See the HilNode.h file for details on what each flag. If any of those flags are active the red LED will be lit as well.
To initiate HIL, start the HIL simulation model. At this point the amber LED on the HILNode should be blinking at twice its normal rate. The controller's GPS LED should also go green as it's receiving good GPS data from the simulator. And finally, on the simulator side it can be checked by looking in /HIL Interface at the latency display at the bottom (this should be very low single digits for the simulation results to be good).
Now to actually begin the simulation, load the desired mission waypoints, set the throttle, and switch to autonomous mode using QGroundControl.
## Full HIL
Full HIL differs from Half HIL only in the connection of the PrimaryNode to the actuators. This can be done onboard the vessel or in a controlled lab setting with a rudder and propeller model. The HILNode detects the data transmit by the rudder node and the ACS300 automatically, so no changes to the PrimaryNode, HILNode, or simulator need to be made in the transition to Full HIL. With the addition of the actuators be sure to run through any necessary calibration procedures as well.
## Additional simulators
The above three simulations are all that is required for testing the vehicle and prepping for another launch. The following simulators add additional debugging and testing capabilities that are not directly required for a launch but can be helpful.
These simulators all rely on real data from actual launches. Depending on the dataset the initialization routines they use (*_sim_init.m) may require modification. The data is chosen based on a CSV file produced from a MAVLink datastream that has all the required messages and the number of the autonomous run contained within that recording. These are easy to find using the static_plots.m script provided in the /Code/Libs/MATLAB folder. And further analysis of a particular autonomous run can be done with the dynamic_plots.m script.
### Plant_sim.mdl
This file implements a simulator for testing the Plant in open-loop on real data from an autonomous section of a real boat launch. The goal of this simulator would be for the Plant and the actual recorded data to be identical. Running this model prompts the user for a file and an autonomous run section to analyze. The results can be displayed and analyzed with the Plant_sim_visualize.m script.
### Replay_sim.mdl
To test new controller modifications, the Replay simulator can be used. It is easy to make modifications to the controller and test them in simulation on real data. Running this model works similarly to the Plant simulator: the user is prompted for a CSV file and an autonomous run number.
Note that this model doesn't use a model reference for the controller block, because it needs access to data within the model and Simulink prevents that. This means that changes done to this model or the controller need to be manually copied to the other.
# SeaSlug Resources
## Physical
- The BotCave contains a variety of non-necessary and weatherproof components.
- Under the drill presses in lab are boxes containing various components.
- The main mast resides in the corner of the lab
- Above the cabinets are tubs and additional supplies.
- The SeaSlug and its trailer are located behind E2, by the woodshop at the fire road entrance. GPS 37.001751,-122.062113
## Code & Data
- The main code repository for the SeaSlug is: https://github.com/Susurrus/Autoboat
- A Simulink library used in the Autoboat repo is: https://github.com/Susurrus/MicroSimulink-Library
- Additional data is stored on the Byron server at /data/projects/SeaSlug/
- The wiki has pictures and reference material: http://byron.soe.ucsc.edu/wiki/autoboat/
- The CANode and its associated hardware are in a repo on Byron as well: ASL_eCAD.git
- QGroundControl is at https://github.com/mavlink/qgroundcontrol.
- MAVLink is at https://github.com/mavlink/mavlink. This isn't necessary to download, as the generated files are stored in the Autoboat repository.
- The datalogger code is at: https://github.com/Susurrus/SLUGS-Logger
- Current code for the Tokimec IMU is at: https://github.com/Susurrus/tokimec
- Potential future IMU code is at: https://github.com/FrauBluher/MPU60xx
- A now-unused serial/UDP software bridge exists at: https://github.com/Susurrus/serial2udp
- The repository for the CANaconda USB-CAN adapter is at: https://github.com/xela144/CANaconda
- The repository for Bryant's Ph.D. dissertation on the SeaSlug is at: https://github.com/bwmairs/dissertation

# Driving Directions

# The Groundstation Computer System (GCS)
  - QGroundControl can be started from the shortcut on the taskbar, which is a shortcut to the release build of QGC.
  - No data should be permanently stored on the groundstation. It should be assumed that it can be reformatted at any time. So all data should be backed up immediately upon returning from a launch.
  - The default user is 'asl'. There is no password and they have administrator rights.
  - Other useful tools installed are Git and Saleae's Logic.
  - All code is stored in ~/Projects.
  - The computer needs a connection to the Logitech F710 controller and the 3DR radios for controlling the SeaSlug and require the black 4-port USB hub.
  - All GCS parts are sealed in a heavy-duty plastic bag for weatherproofing during launches. This bag then velcros into the blue chassis.
  - When launching the power setting should be set to Balanced. This turns the screen brightness all the way up, prevents it from sleeping, but turns off the screen after 2 minutes.
  - Since the GCS is sealed it is prone to overheating leave covered when not in use.
  - QGroundControl has been compiled with audio output, so either a Bluetooth headset, headphones, or the built-in speakers can be used with it.
  - The power button does not do anything when the computer is on, it's been disabled. It does, however, turn it on.
  - The touch screen has been disabled as the expected input method is through a Wacom-compatible pen.
# Using QGroundControl
- These instructions assume you have built QGC with the “seaslug” messageset as defined within the Autoboat repository and the audio interface. All other optional components should be disabled (for performance and compilation speed reasons).
- To connect to the SeaSlug have a wired or wireless serial connection to the main GCS datastream. The datalogger stream will still register in QGC, but it's only telemetry output.
- Make sure the Logitech F710 controller is connected. Insert the controller's USB transceiver and press the center silver Logitech button to start the connection process. The LED should blink briefly and then go solid. Once the gamepad is connected pressing the bottom-left “Mode” button will toggle the LED next to it on and then off (leave it off).
- Open QGroundControl and enable manual control of the SeaSlug by going to File→Settings→Joystick and enabling it. If the gamepad doesn't appear, repeat the above directions. Configure the joystick so that: the up-down motion of the left thumbstick is inverted throttle, the left-right motion of the left thumbstick is inverted yaw, and Button 9 is set to “Toggle Autonomy”. The rudder calibration button is not a QGC mapping, but is hard-coded into the SeaSlug controller.
- If this is the first time running QGroundControl, press the “Connect” button in the upper right to open the Connections Manager. Create a new serial connection on the proper port at 115200baud and hit “Connect.”
- If the serial connection already exists, hit “Connect”.
- MAV20 should appear, which is the SeaSlug.
- When finished with QGC, closing the program or hitting the “Disconnect” button will open a dialog prompting you to save the log file. The default location is ~/Documents/QgroundControl/FlightData.
# Processing recorded MAVLink data
The process for extracting data relies on the tools within the MAVLink project and Python. While MAVLink is partially compatible with Python3, sometimes there are issues so Python2.7 is recommended. It should be downloaded and exist on the $PYTHONPATH. Additionally the seaslug.xml message definition file from the Autoboat repository should exist in the $MAVLINK_DIR/message_definitions/v1.0/ directory. With that set up all MAVLink scripts can be run like:
python -m pymavlink.tools.*
## Extracting groundstation data
1. QGroundControl saves recorded MAVLink data with 64-bit Unix timestamps embedded in it which is how the following PyMAVLink tools extract time information.
2. Extracting a CSV file can be done with PyMAVLink's mavlogdump tool:

   python -m pymavlink.tools.mavlogdump --dialect=seaslug --format=csv --types=COMMA,SEPARATED,LIST,OF,MESSAGES LOG_FILENAME.mavlink > LOG_FILENAME.csv
3. This CSV file can then be imported into MATLAB using the ProcessCsvFile MATLAB function provided in the Autoboat repository at /Code/Libs/MATLAB/. Like:

   data = ProcessCsvFile('LOG_FILENAME.csv');
4. Note that when this CSV file is imported, it'll have NaNs when the message didn't have data. These can be easily filtered with MATLAB's isnan function.
## Extracting datalogger data
1. Run the Python script from the SLUGS-Logger project's Testing/extractData.py script, giving it the XXXX.log file recorded from the datalogger. This will create a XXXX_extracted.log file. Rename it to XXXX.mavlink for clarity. It may spit out some errors, but those are common because of how the datalogger generates file and can almost always be safely ignored.
2. Follow the instructions for extracting data from the groundstation datastream except add the --no-timestamps argument to the call to mavlogdump, because the datalogger doesn't inject timestamps into its recorded datastream.
## Additional tools
Once data is in a CSV format, see the MATLAB functions available in the Autoboat repository at: /Code/Libs/MATLAB/ and /Code/Scripts/MATLAB/.

For working with data still in MAVLink format, see the various tools offered in the MAVLink repository's pymavlink library at /pymavlink/tools/. Especially useful are mavloss and mavsummarize.
# Node status/error bits and LEDs
## Primary node
LEDs
Amber	Blinks at 1Hz
Red	System is in a reset state. See the Error bits below.
GPS	Solid when there is a good GPS connection. / Blinks at 4Hz when no good GPS data is being received. / Nothing when the GPS is disconnected.
Auto	Solid when the system is in autonomous mode. / Blinking at 4Hz when in autonomous mode and overridden by the backup manual controller.

Status bits		Error bits
0x0001	Vehicle is under autonomous control.	0x0001	Active during the first 5 seconds of bootup.
0x0002	System is in return-to-base mode.	0x0002	The groundcontrol station has been disconnected for >= 30s.
0x0004	ECAN peripheral in the transmission error state.	0x0004	The GPS unit has had a bad fix for >= 10s.
0x0008	ECAN peripheral in the reception error state.	0x0008	The DST800 water speed sensor is disconnected
0x0010	The GPS is no longer giving good readings	0x0010	Manual override has been engaged by the secondary controller.
0x0020	The RC node is missing from the CAN bus.	0x0020	The rudder is undergoing calibration.
		0x0040	The rudder is uncalibrated.
		0x0080	The system is in emergency-stop mode, actuators are centered and stopped, system will not respond to any commands; it's dead in the water. This can also occur if the CAN connection to the ACS300 is lost/unavailable.
		0x0100	The IMU is disconnected.
		0x0200	The rudder is disconnected.
		0x0400	Return-to-base mode has been engaged due to an error condition.

## RC node
LEDs
Amber	Blinks at 1Hz normally. / Double-blinks at 1Hz when the transmitter is connected.
Red	System is in a reset state OR a fatal error has occurred. See the Error bits below.
Transmitter	Solid when the RC transmitter is on and connected.

Status bits		Error bits
0x0001	The RC transmitter is connected and in manual control mode	0x0001	The ACS300 is not detected or the e-stop is active.
0x0002	The RC transmitter is connected	0x0002	The RC node is uncalibrated.
		0x0004	ECAN peripheral in the transmission error state.
		0x0008	ECAN peripheral in the reception error state.

## Rudder node
LEDs
Amber	Blinks at 10Hz while uncalibrated. / Blinks at 4Hz while calibrating. / Blinks at 1Hz once calibrated.
Red	A fatal error has occurred.

Status bits		Error bits
0x0001	Rudder is calibrated.
0x0002	System is calibrating.
0x0004	The starboard limit is being triggered.
0x0008	The port limit is being triggered.

## IMU node
LEDs
Amber	Blinks at 1Hz normally. / Blinks at 2Hz when the IMU is connected and messages are being successfully decoded.
Red

Status bits		Error bits
0x0001	The IMU is actively transmitting.